## Slide 1: Introduction of Socle Technology
Presenter:
1/17/24

## Slide 2
Channel Service

## Slide 3: World Wide Sales Channel：Locations and Values
Socle Sales Office
Socle Reps / Distributors
Global online Distributors
Representing Foxconn Group Brands at several regions
Plenty connections, sales routes around the world
Experienced FAE in consumer electronics, such as Air purifier, Camera, Distance ranging, Robot…etc.
Leveraging engineering resource in Foxconn group for building up sensor modules
Notes: Socle藉由銷售Sharp電子原器件產品,在各個區域建立起相關的銷售渠道以及當地的銷售人員. 在銷售鴻海集團產品的同時,也在世界各地尋找有競爭力的產品,試圖帶回集團做出貢獻
Socle有建立起FAE團隊,專精於消費性產品。
Socle同時也可利用鴻海集團的工程資源, 能將傳給器組成模組, 或者是將模組在更進一步組成系統的能力。
負責區域: 中國、美國 、東南亞、印度
自有Office:上海、杭州、深圳、台灣、加拿大

## Slide 4
Power Isolation
Photo coupler
Gate Driver
Sensors
Photo-interrupter
Distance Measurement Sensor
TOF sensor & module
PM2.5 sensor
MEMS Mic
Wi-Fi 4/5/6 (+BT) Wireless Module
Laser
Laser Diode
Sensing
Computing
Communication
Control
Product Line
Power Semiconductor
SiC MOSFET
Notes: To247 想個圖 一個晶圓

## Slide 5
Power Semiconductor

## Slide 6: Power Semiconductor – SiC MOSFET
Item | Parameter | 
Drain-Source Breakdown Voltage | 1200 | 1700V
RDS | 12, 16, 20, 40, 70mohm | 40mohm, 1ohm, 50ohm
Guaranteed performance over temperature | 25°C ~ +175°C. | 
Applications
Features
Battery Chargers
Industrial Inverter
DC/DC converters

## Slide 7: Power Semiconductor – SiC MOSFET Product List
Emerald series | Gen 1 |  |  |  |  | Gen 2
 | 1200V |  |  |  |  | 
 | 12mohm | 16mohm | 20mohm | 40mohm | 70mohm | 16mohm
Drain-Source Breakdown Voltage (BV) | 1200V | 1200V | 1200V | 1200V | 1200V | 1200V
Gate-source threshold voltage (Vth) | 2.9V | 2.9V | 2.9V | 2.9V | 2.9V | 3V
Drain-source on-state resistance (Ron) | 12mohm | 16mohm | 20mohm | 40mohm | 70mohm | 16mohm
Continuous DC drain current (Id) | 125A | 105A | 85A | 55A | 35A | 100A
Gate-to-drain charge (Qgd) | 95nc | 69nc | 55nc | 35nc | 27nc | 94nc
Rutile series Gen 2 | 1200V |  |  |  | 
 | 12mohm | 16mohm | 20mohm | 40mohm | 70mohm
Drain-Source Breakdown Voltage (BV) | 1200V | 1200V | 1200V | 1200V | 1200V
Gate-source threshold voltage (Vth) | 2.9V | 2.9V | 2.9V | 2.9V | 2.9V
Drain-source on-state resistance (Ron) | 12mohm | 16mohm | 20mohm | 40mohm | 70mohm
Continuous DC drain current (Id) | 135A | 110A | 90A | 55A | 35A
Gate-to-drain charge (Qgd) | 94nc | 70nc | 55nc | 28nc | 16nc

## Slide 8
Power Isolation

## Slide 9: Power Isolation - Gate Driver Photocoupler
Cathode
VO
VSS
Anode
VCC
Item | Parameter
Maximum peak output current | 0.8A, 1A, 3A, 4A
Rail-to-rail output voltage | Yes
Maximum propagation delay | 110 ns
Under Voltage Lock-Out protection (UVLO) with hysteresis | Yes
Wide operating range | 10 to 30 Volts (VCC)
Guaranteed performance over temperature | -40°C ~ +110°C.
Safety approval | UL, VDE, CQC
Applications
Features
AC brushless
Induction Heating
Industrial Inverter

## Slide 10: Power Isolation - Gate Driver Photocoupler
Selection Table |  |  |  |  |  |  | 
Part number | Package | Status | Peak Output Current (A) | Viso (Vrms) | VCC (V) | TPLH/TPHL (Max) | TOPR (℃)
FSS-5701P/W-T1V | LSOP6 | MP | 0.8 | 5000 | 10 ~ 30 | 110ns | -40 ~ 110
FSS-314P/W-T1V | LSOP6 | MP | 1 | 5000 | 10 ~ 30 | 110ns | -40 ~ 110
FSS-341P/W-T1V | LSOP6 | MP | 3 | 5000 | 15 ~ 30 | 110ns | -40 ~ 110
FSS-343P/W-T1V | LSOP6 | MP | 4 | 5000 | 15 ~ 30 | 110ns | -40 ~ 110
Gate Driver |  |  |  | 
Part number | Package | Feature | BROADCOM | TOSHIBA
FSS-5701P/W-T1V | LSOP6 | 0.8A | --- | ---
FSS-314P/W-T1V | LSOP6 | 1A | ACPL-P314 | TLP5701
FSS-341P/W-T1V | LSOP6 | 3A | ACPL-P341 | TLP5754
FSS-343P/W-T1V | LSOP6 | 4A | ACPL-P343 | TLP5754
Cross Reference

## Slide 11: Photocoupler - High Speed
NC 1
Cathode 3
6 VO
5 GND
NC 4
Anode 2
8 VCC
Item | Parameter
Switching Speed | 1M & 10M bit/s Max
High isolation | 5000 VRMS
DC input with logic gate output | Yes
Operating temperature range | - 55 °C to 100 °C
MSL | Class 1
  Ground loop elimination
  LSTTL to TTL
  LSTTL or CMOS
  Line receiver
  data transmission
  Switching power supply
  Pulse transformer replacement
  Computer peripheral interface
7 VE
Applications
Features

## Slide 12: Photocoupler - High Speed
Selection Table |  |  |  |  |  |  | 
Part number | Package | Status | Feature | Viso (Vrms) | VCC (V) | TPLH/TPHL (Max) | TOPR (℃)
FSS-480P/W-T1V | LSOP6 | MP | IPM, Positive output | 5000 | 35 | 250ns | -55~110
FSS-481P/W-T1V | LSOP6 | MP | IPM, Negative output | 5000 | 35 | 250ns | -55~110
FSS-611P/W-T1V | LSOP6 | MP | 10M | 5000 | 3.3/5 | 75ns | -40~110
FSS-50LP/W-T1V | LSOP6 | MP | 1M | 5000 | 3.3/5 | 75ns | -40~110
High Speed |  |  |  | 
Part number | Package | Feature | BROADCOM | TOSHIBA
FSS-480P/W-T1V | LSOP6 | IPM, Positive output | ACPL-P480 | TLP2710
FSS-481P/W-T1V | LSOP6 | IPM, Negative output | ACPL-P481 | TLP2710
FSS-611P/W-T1V | LSOP6 | 10M High Speed | ACPL-P483 | TLP2748
FSS-50LP/W-T1V | LSOP6 | 1M High Speed | ACPL-W50L | TLP2719 (LF4)
Cross Reference

## Slide 13: Photocoupler - Phototriac
Anode 1
Cathode 2
5 Substrate
4 Terminal
NC 3
6 Terminal
Item | Parameter
High isolation | 5000 VRMS
DC input with zero-cross / random-phase photo triac output | v
Operating temperature range | - 40 °C to 100 °C
REACH & RoHS compliance | v
MSL | Class 1
Safety approval | UL, VDE, and CQC
Solenoid / valve controls
Lighting controls
Motor controls
Temperature controls
Static AC power switches
Solid state relays
Interfacing microprocessors to 115 to 240V AC peripherals
Applications
Features
Notes: Description
  The 305X and 306X series combine an AlGaAs infrared emitting diode as the emitter which is optically coupled to a monolithic silicon random-phase photo triac in a plastic DIP6 package with different lead forming options.

## Slide 14: Photocoupler - Phototriac
Selection Table |  |  |  |  |  |  | 
Part number | Package | Status | Feature | Viso (Vrms) | VCC (V) | TPLH/TPHL (Max) | TOPR (℃)
FSS-305XP/W-T1V | DIP6 | MP | Z.C | 5000 | 15,10,5 | 600 | 55~110
FSS-306XP/W-T1V | DIP6 | MP | R.P | 5000 | 15,10,5 | 600 | 55~110
Part number | Package | Applied voltage | Feature |  | ON-state current
S2S3A00F / S2S5A00F / S2S5FA0F | Mini-flat 4-pin | AC 200 V lines | 200 V lines, compact |  | 0.05 A
S2S4A00F | Mini-flat 4-pin | AC 200 V lines | 200 V lines, compact | Built-in zero-cross circuit | 0.1 A
PC3SH11YFZAH / PC3SH13YFZAH | DIP4 | AC 200 V lines | Reinforced isolation |  | 0.1 A
PC3SH21YFZBH | DIP4 | AC 200 V lines | Reinforced isolation | Built-in zero-cross circuit | 0.1 A
PC3SD12NTZAH / PC3SD11NTZBH / PC3SD11NTZCH | DIP4 | AC 200 V lines | General purpose |  | 0.1 A
PC3SD21NTZAH / PC3SD21NTZBH / PC3SD21NTZDH | DIP6 | AC 200 V lines | Reinforced isolation | Built-in zero-cross circuit | 0.1 A
PC3SF11YVZAH / PC3SF11YVZBH | DIP6 | AC 200 V lines | Reinforced isolation |  | 0.1 A
PC3SF21YVZAH / PC3SF21YVZBH | DIP6 | AC 200 V lines | General purpose | Built-in zero-cross circuit | 0.1 A
PC4SD11NTZCH | DIP6 | AC 200 V lines | General purpose |  | 0.1 A
PC4SD21NTZCH / PC4SD21NTZDH | DIP6 | AC 200 V lines | Reinforced isolation | Built-in zero-cross circuit | 0.1 A
PC4SF11YTZBH | DIP6 | AC 200 V lines | Reinforced isolation |  | 0.1 A
PC4SF21YVZBH / PC4SF21YWPSH | DIP6 | AC 200 V lines |  | Built-in zero-cross circuit | 0.1 A

## Slide 15: Power Isolation - Photocoupler
Item | Parameter
Double transfer mold package | DIP4, DIP8
High collector-emitter voltage | VCEO : 80V
High isolation voltage between input and output | 5 kV
Current transfer ratio | 50%
Safety approval | UL, VDE, CQC
Programmable controller
Facsimiles
Telephones
Applications
Features
Garage door opener
Process control
Notes: ＊北美賣哪些大客人 換

## Slide 16: Power Isolation - Photocoupler - Transistor output
Selection Table |  |  |  | 
Part number | Package | Output type | Feature | 
PC357NJ0000F / PC451J00000F | Mini-flat 4-pin | Single phototransistor | High collector-emitter voltage | 
PC367NJ0000F | Mini-flat 4-pin | Darlington phototransistor | AC input response | Low input current
PC354NJ0000F | Mini-flat 4-pin | Darlington phototransistor | AC input response | 
PC364NJ0000F | Mini-flat 4-pin | Darlington phototransistor | High sensitivity, High collector-emitter voltage | Low input current
PC355NJ0000F / PC452J00000F | Mini-flat 4-pin | Darlington phototransistor | High sensitivity, High collector-emitter voltage | 
PC365NJ0000F | Mini-flat 4-pin | Single phototransistor | General purpose | Low input current
PC3H7J00001H | Compact half pitch | Single phototransistor | General purpose | 
PC3HU7xYIP1B | Compact half pitch | Single phototransistor | AC input response | Reinforced insulation
PC3H71xNIP1H | Compact half pitch | Single phototransistor | AC input response | Low input current
PC3H3J00001H / PC3H4J00001H | Compact half pitch | Single phototransistor | AC input response | 
PC123XxYSZ1B | DIP4 | Single phototransistor | Reinforced insulation | 
PC1231xNSZ1B | DIP4 | Darlington phototransistor | High collector-emitter voltage | Low input current
PC817XxNSZ1B / PC851XNNSZ1H | DIP4 | Darlington phototransistor | High collector-emitter voltage | 
PC8171xNSZ1B | DIP4 | Darlington phototransistor | High sensitivity, High collector-emitter voltage | Low input current
PC852XNNSZ1H | DIP4 | Darlington phototransistor | High sensitivity, High collector-emitter voltage | 

## Slide 17: Power Isolation - Photocoupler - OPIC output
Selection Table |  |  |  | 
Part number | Package | Output type | Feature | 
PC400J00000F / PC410LENIP0F | Mini-flat 5-pin | Digital output | General purpose, High response speed | 
PC457L0NIP0F | Mini-flat 5-pin | Analog/Digital output | High CMR | 
PC923LRNSZ0F | DIP8 | Built-in base amplifier | For inverter control | 1.5A output
PC925LENSZ0F | DIP8 | Built-in base amplifier | For inverter control | 2.5A output

## Slide 18: Power Isolation - Solid State Relay
Item | Parameter
Zero crossing functionary | VOX : MAX. 35V
High repetitive peak off-state voltage | VDRM : 400V ; 600V
High isolation voltage between input and output | Viso( rms ) : 4.0kV
Superior noise immunity | dV/dt : MIN. 100V/µs
Safety approval: | UL, VDE, CQC
Heaters
Fans
Motors
Applications
Features
White Goods
Notes: 白電 替換

## Slide 19: Power Isolation - Solid State Relay
Selection Table |  |  |  | 
Part number | Package | Applied voltage | Feature | ON-state current
PR31MA11NTZH | DIP6 | AC 200 V lines | General purpose | 0.06 A
PR32MA11NTZH | DIP6 | AC 200 V lines | General purpose | 0.15 A
PR33MF5 series / PR36MF5 series / PR39MF5 series / PR3BMF5 series | DIP8 | AC 200 V lines | General purpose | 0.3 / 0.6 / 0.9 / 1.2 A
PR36MF2 series / PR39MF2 series | DIP8 | AC 200 V lines | Built-in zero-cross circuit | 0.6 / 0.9 A

## Slide 20
Laser Diode

## Slide 21: Laser Diode - UV / Blue
biologically relevant
Particle Counter
VR/AR
ø9 mm Can
ø5.6 mm Can
ø3.8 mm Can
ø3.3 mm Can
t1.8 mm Frame
Applications
Features
Item-UV laser Diode | Parameter
Can Package | ø5.6 mm
Wavelength (nm) | 395 nm ~ 406 nm
Absolute Maximum rating Po (mW) | 1100 mW
Absolute Maximum rating Iop (mA) | 650 mA
Item-Blue laser Diode | Parameter
Can Package | ø3.8 mm , ø5.6 mm, ø9 mm
Wavelength (nm) | 435 nm ~ 487 nm
Absolute Maximum rating Po (mW) | 2000 mW
Absolute Maximum rating Iop (mA) | 4300 mA
Life Sciences related

## Slide 22: Laser Diode - UV / Blue
Selection Table |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Color | Part No. | Wavelength(Peak)Ap(nm) | Absolute maximum rating*1 Po(mW) | Absolute maximum rating*1 Iop(mA) | Absolute maximum rating*1 Top(C) | Po(mW) | Ith(mA) | lop(mA) | Vop(V) | ηd(mW/mA) | λp(nm) | Θ//(°) | Θ⊥(°) | FFP | Packaging | Monitor PD (Built-in:O)
UV | GH0393AA2G | 395 | 350 | - | O to +30 | 300 | 150 | 310 | 4.4 | 1.8 | 395 | 13 | 44 | *3 | ø5.6 | -
UV | GH0401FA2G | 405 | 155 | - | -10 to +75 | 150 | 40 | 130 | 5 | 1.7 | 405 | 9 | 19 | *2 | ø5.6 | -
UV | GH0401FA2K | 405 | 155 | - | -10 to +75 | 150 | 40 | 130 | 5 | 1.7 | 405 | 9 | 19 | *2 | ø5.6 | O
UV | GH04W10A2GC | 406 | 350 | - | 0 to +50 | 300 | 140 | 325 | 4.5 | 1.8 | 406 | 14 | 41 | *3 | ø5.6 | -
UV | GH0406AA2G | 405 | 700 | - | O to +30 | 600 | 120 | 420 | 4.4 | 2 | 405 | 16 | 38 | *3 | ø5.6 | -
UV | GH04V01A2G | 405 | 1100 | - | O to +30 | 1000 | 125 | 625 | 5 | 2 | 405 | 16 | 40 | *3 | ø5.6 | -
Blue | GH04C05W9G | 435 | - | 3600 | O to +45 | 5000 | 350 | 3100 | 4.5 | 1.8 | 435 | 9 | 47 | *3 | ø9.0 | -
Blue | GH04C05W9G | 435 | - | 3000 | 45 to +60 | 5000 | 350 | 3100 | 4.5 | 1.8 | 435 | 9 | 47 | *3 | ø9.0 | -
Blue | GH04C05V9G | 440 | - | 3500 | 0 to +35 | 5000 | 350 | 3100 | 4.6 | 1.9 | 440 | 10 | 47 | *3 | ø9.0 | -
Blue | GH04C03Z9G | 450 | - | 2800 | O to +60 | 3500 | 260 | 2100 | 4.4 | 1.85 | 450 | 9 | 47 | *3 | ø9.0 | -
Blue | GH04C06X9G | 450 | - | 4300 | O to +60 | 6000 | 300 | 4000 | 4.8 | 1.55 | 450 | 9 | 48 | *3 | ø9.0 | -
Blue | GH04580A2G | 450 | 85 | - | -10 to +70 | 80 | 22 | 84 | 5.1 | 1.3 | 450 | 10 | 24 | *2 | ø5.6 | -
Blue | GH04C01A2G | 450 | 1650 | - | -10 to +50 | 1600 | 200 | 1200 | 5 | 1.5 | 450 | 6.5 | 23 | *2 | ø5.6 | -
Blue | GH04C01B2G | 450 | 2000 | - | -10 to +50 | 1800 | 110 | 1100 | 4.1 | 1.8 | 450 | 7 | 26 | *2 | ø5.6 | -
Blue | GH04590A5G | 450 | 95 | - | -10 to +50 | 90 | 28 | 100 | 5.2 | 1.3 | 450 | 9 | 24 | *2 | ø3.8 | -
Blue | GH04850B2G | 487 | 55 | - | -10 to +60 | 50 | 40 | 105 | 6 | 0.8 | 487 | 8 | 23 | *2 | ø5.6 | -
ø9 mm Can
ø5.6 mm Can
ø3.8 mm Can
ø3.3 mm Can
t1.8 mm Frame

## Slide 23: Laser Diode - Green / Red
Robotic pool cleaner
Life Sciences related
Projector
ø9 mm Can
ø5.6 mm Can
ø3.8 mm Can
ø3.3 mm Can
t1.8 mm Frame
Applications
Features
Item-Green laser Diode | Parameter
Can Package | ø3.8 mm , ø5.6 mm, ø9 mm, t1.8 mm
Wavelength (nm) | 515 nm ~ 520 nm
Absolute Maximum rating Po (mW) | 135 mW
Absolute Maximum rating Iop (mA) | 1650 mA
Item-Red laser Diode | Parameter
Can Package | ø3.3 mm ,ø3.8 mm, ø5.6 mm, ø9 mm, t1.8 mm
Wavelength (nm) | 638 nm ~ 660nm
Absolute Maximum rating Po (mW) | 1210 mW
Absolute Maximum rating Iop (mA) | 1600 mA
Laser Distance Meter
Measuring Device

## Slide 24: Laser Diode - Green
Selection Table |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Color | Part No. | Wavelength(Peak)Ap(nm) | Absolute maximum rating*1 Po(mW) | Absolute maximum rating*1 Iop(mA) | Absolute maximum rating*1 Top(C) | Po(mW) | Ith(mA) | lop(mA) | Vop(V) | ηd(mW/mA) | λp(nm) | Θ//(°) | Θ⊥(°) | FFP | Packaging | Monitor PD (Built-in:O)
Green | GH15230H8C | 515 | 35 | - | -10 to +60 | 30 | 30 | 90 | 7 | 0.5 | 515 | 7.5 | 22 | *2 | t1.8 | -
Green | GH05230H2KC | 520 | 35 | - | -10 to +60 | 30 | 25 | 70 | 6.5 | 0.65 | 520 | 7 | 22 | *2 | ø5.6 | O
Green | GH05250F2K | 520 | 55 | - | -10 to +60 | 50 | 40 | 100 | 5.9 | 0.7 | 520 | 7 | 22 | *2 | ø5.6 | O
Green | GH05280E2KC | 520 | 85 | - | -10 to +60 | 80 | 50 | 150 | 6.5 | 0.8 | 520 | 7 | 23 | *2 | ø5.6 | O
Green | GH05280E5K | 520 | 85 | - | -10 to +60 | 80 | 65 | 180 | 6.5 | 0.7 | 520 | 7 | 23 | *2 | ø3.8 | O
Green | GH0521DE2G | 520 | 135 | - | -10 to +60 | 130 | 70 | 270 | 6.7 | 0.65 | 520 | 8 | 22 | *2 | ø5.6 | -
Green | GH05290A5G | 520 | 95 | - | -10 to +50 | 90 | 60 | 185 | 6.75 | 0.7 | 520 | 7 | 23 | *2 | ø3.8 | -
Green | GH0521DE5G | 520 | 135 | - | -10 to +50 | 130 | 70 | 270 | 6.7 | 0.65 | 520 | 8 | 22 | *2 | ø3.8 | -
Green | GH0523AD2G | 520 | - | 850 | O to +60 | 300 | 100 | 500 | 5.2 | 0.75 | 520 | 7 | 23 | *2 | ø5.6 | -
Green | GH05C01A9G | 520 | - | 1400 | O to +60 | 600 | 180 | 1050 | 5.2 | 0.7 | 520 | 9 | 44 | *3 | ø9.0 | -
Green | GH05C01C9G | 520 | - | 2000 | O to +60 | 1000 | 250 | 1650 | 5.2 | 0.7 | 520 | 9 | 45 | *3 | ø9.0 | -
ø9 mm Can
ø5.6 mm Can
ø3.8 mm Can
ø3.3 mm Can
t1.8 mm Frame

## Slide 25: Laser Diode - Red
Selection Table |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Color | Part No. | Wavelength(Peak)Ap(nm) | Absolute maximum rating*1 Po(mW) | Absolute maximum rating*1 Iop(mA) | Absolute maximum rating*1 Top(C) | Po(mW) | Ith(mA) | lop(mA) | Vop(V) | ηd(mW/mA) | λp(nm) | Θ//(°) | Θ⊥(°) | FFP | Packaging | Monitor PD (Built-in:O)
Red | GH06C01A9G | 640 | 1210 | 1600 | O to +45 | 1200 | 350 | 1400 | 2.25 | 1.15 | 640 | 11 | 35 | *2 | ø9.0 | -
Red | GH06C02B9G | 640 | - | (tbd) | O to +55 | 2500 | 600 | 2800 | 2.4 | 1.1 | 639 | 15 | 70 | *3 | ø9.0 | -
Red | GH06330A2G | 638 | 30 | - | -10 to +60 | 30 | 30 | 50 | 2.3 | 1.4 | 638 | 7 | 16 | *2 | ø5.6 | -
Red | GH0631IA2GC | 638 | 185 | - | -10 to +60 | 180 | 70 | 215 | 2.55 | 1.15 | 638 | 8 | 13 | *2 | ø5.6 | -
Red | GH0632BA2GC | 638 | 210 | - | -10 to +60 | 200 | 55 | 230 | 2.65 | 1.15 | 639 | 8 | 15 | *2 | ø5.6 | -
Red | GH0637AA2G | 638 | 702 | - | -10 to +40 | 700 | 110 | 810 | 2.46 | 1 | 638 | 16 | 35 | *2 | ø5.6 | -
Red | GH0631CA5GC | 638 | 120 | - | -10 to +60 | 120 | 50 | 150 | 2.5 | 1.2 | 638 | 8 | 15 | *2 | ø3.8 | -
Red | GH0631IA5G | 638 | 185 | - | -10 to +60 | 150 | 60 | 190 | 2.5 | 1.15 | 638 | 7.5 | 15 | *2 | ø3.8 | -
Red | GH1631AA8C | 638 | 100 | - | -10 to +60 | 100 | 50 | 130 | 2.45 | 1.2 | 638 | 8 | 15 | *2 | t1.8 | -
Red | GH0652CA2GC | 650 | 220 | - | -10 to +70 | 200 | 55 | 220 | 2.6 | 1.2 | 650 | 8 | 12.5 | *2 | ø5.6 | -
Red | GH06610A2KC | 660 | 12 | - | -40 to +90 | 10 | 15 | 24 | 2.2 | 1.1 | 660 | 12 | 33 | *2 | ø5.6 | O
Red | GH06P25A2CC | 660 | 100 | - | -10 to +70 | 95 | 40 | 122 | 2.4 | 1.1 | 660 | 10 | 15.5 | *2 | ø5.6 | -
Red | GH06510F4A | 660 | 10 | - | -10 to +70 | 7 | 17 | 26 | 2.2 | 0.85 | 660 | 13 | 28 | *2 | ø3.3 | O
Red | GH16P32B8C | 660 | 100 | - | -10 to +70 | 90 | 42 | 120 | 2.3 | 1.16 | 661 | 9.3 | 15 | *2 | t1.8 | -
ø9 mm Can
ø5.6 mm Can
ø3.8 mm Can
ø3.3 mm Can
t1.8 mm Frame

## Slide 26: Laser Diode - IR
biologically relevant
Range Finder
ø9 mm Can
ø5.6 mm Can
ø3.8 mm Can
ø3.3 mm Can
t1.8 mm Frame
Applications
Features
Item-IR laser Diode | Parameter
Can Package | ø3.3 mm , ø5.6 mm
Wavelength (nm) | 785 nm ~ 940 nm
Absolute Maximum rating Po (mW) | 260 mW
Absolute Maximum rating Iop (mA) | 300 mA
Life Sciences related

## Slide 27: Laser Diode - IR
Selection Table |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Color | Part No. | Wavelength(Peak)Ap(nm) | Absolute maximum rating*1 Po(mW) | Absolute maximum rating*1 Iop(mA) | Absolute maximum rating*1 Top(C) | Po(mW) | Ith(mA) | lop(mA) | Vop(V) | ηd(mW/mA) | λp(nm) | Θ//(°) | Θ⊥(°) | FFP | Packaging | Monitor PD (Built-in:O)
IR | GH07P28F4C | 785 | 150 | - | -10 to +70 | 100 | 35 | 135 | 2.4 | 1 | 784 | 8 | 16 | *2 | ø3.3 | -
IR | GH0832BA2K | 830 | 210 | - | -10 to +70 | 200 | 35 | 215 | 2.1 | 1.1 | 830 | 9 | 16 | *2 | ø5.6 | O
IR | GH0832FA2G | 830 | 260 | - | -10 to +70 | 250 | 48 | 260 | 2.2 | 1.15 | 830 | 8 | 13.5 | *2 | ø5.6 | -
IR | GH0852WA2G | 850 | 700 | - | -10 to +70 | 700 | 230 | 900 | 2 | 1 | 850 | 13.5 | 45 | *3 | ø5.6 | -
IR | GH0942FA2G | 940 | 260 | - | -10 to +70 | 250 | 45 | 300 | 2.4 | 0.97 | 940 | 8 | 14 | *2 | ø5.6 | -
IR | GH0942WA2G | 940 | 700 | - | -10 to +70 | 700 | 200 | 1000 | 2 | 0.9 | 940 | 15 | 45 | *3 | ø5.6 | -
ø9 mm Can
ø5.6 mm Can
ø3.8 mm Can
ø3.3 mm Can
t1.8 mm Frame

## Slide 28
MEMS Microphones

## Slide 29: MEMS Microphones
Item | Parameter
Own IC | YES
Own IP | YES
Has ANC | YES
Support High Pressure | YES
Low Power Consumption | YES
Our Own Rnd, Supports Customization | YES
Different Sensor Types + Different ASI Types | YES
Work in high temperature environment
SNR
Tolerance ~±0.25 dB
Automotive
Mobile Phone
Notebooks
Headphones /
TWS
TV
Security
Automotive
flat frequency response  ANC headset、speech recognition
Applications
Features

## Slide 30: MEMS Microphones - Automotive
Item | Parameter
Port | TOP
A/D | Digital
SNR | 64 dB
AOP | 120 dB
Senitivity | -26±1 dBFS
Package | 4.00 x 3.00 x 1.00mm
PN | 3SM227KMT1KA-P
Applications
Features
3SM227KMT1KA-P
Work in high temperature environment
SNR
Tolerance ~±0.25 dB
Automotive

## Slide 31: MEMS Microphones - Automotive
Selection Table |  |  |  |  |  |  | 
P/N | A/D | SNR | AOP | Sensitivity | LFRO | Package | Port
3SM127E4T1UB | Analog | 59 dB | 130 dB | -42±1 dBV | 130 Hz | 3.76 x 2.95 x 1.10mm | Top
3SM127F4T1UE | Analog | 60 dB | 130 dB | -42±1 dBV | <20 Hz | 3.76 x 2.95 x 1.10mm | Top
3SM127MZT1UA | Analog | 66 dB | 130 dB | -38±1 dBV | <20 Hz | 3.76 x 2.95 x 1.10mm | Top
3SM127MZB1UA | Analog | 66 dB | 130 dB | -38±1 dBV | <20 Hz | 3.76 x 3.00 x 1.10mm | Bottom
3SM127LZB1HA | Analog | 65 dB | 130 dB | -38±1 dBV | <20 Hz | 3.50 x 2.65 x 0.98mm | Bottom
3SM227KMT1KA-P | Digital | 64 dB | 120 dB | -26±1 dBFS | 50 Hz | 4.00 x 3.00 x 1.00mm | Top
3SM227KMB1HA-P | Digital | 64 dB | 120 dB | -26±1 dBFS | 50 Hz | 3.50 x 2.65 x 0.98mm | Bottom
3SM127E4T1UB | Analog | 59 dB | 130 dB | -42±1 dBV | 130 Hz | 3.76 x 2.95 x 1.10mm | Top
3SM127F4T1UE | Analog | 60 dB | 130 dB | -42±1 dBV | <20 Hz | 3.76 x 2.95 x 1.10mm | Top
3SM127MZT1UA | Analog | 66 dB | 130 dB | -38±1 dBV | <20 Hz | 3.76 x 2.95 x 1.10mm | Top
3SM127MZB1UA | Analog | 66 dB | 130 dB | -38±1 dBV | <20 Hz | 3.76 x 3.00 x 1.10mm | Bottom
AEC-Q100 is Verification specification for active components
AEC-Q103 is Verification specification for MEMS microphones
Notes: 分類
補足料件

## Slide 32: MEMS Microphone Lineup – Consumer
Selection Table |  |  |  |  |  |  | 
P/N | A/D | SNR | AOP | Sensitivity | LFRO | Package | Port
3SM121JZB1VB-R | Analog | 63 dB | 128 dB | -38±1 dBV | <20 Hz | 2.75 x 1.85 x 0.90mm | Bottom
3SM123B4T1VA-R | Analog | 56 dB | 130 dB | -42±1 dBV | 26 Hz | 2.75 x 1.85 x 0.95mm | Top
3SM123C4T1VA-R | Analog | 57 dB | 123 dB | -42±1 dBV | 63 Hz | 2.75 x 1.85 x 0.95mm | Top
3SM122HZB1VD-R | Analog | 62 dB | 123 dB | -38±1 dBV | 30 Hz | 2.75 x 1.85 x 0.90mm | Bottom
3SM123GZB1VD-R | Analog | 61.5 dB | 123 dB | -38±1 dBV | 20 Hz | 2.75 x 1.85 x 0.90mm | Bottom
3SM123B4T1VA-R | Analog | 56 dB | 130 dB | -42±1 dBV | 26 Hz | 2.75 x 1.85 x 0.95mm | Top
3SM123C4T1VA-R | Analog | 57 dB | 123 dB | -42±1 dBV | 63 Hz | 2.75 x 1.85 x 0.95mm | Top
3SM122HZB1VD-R | Analog | 62 dB | 123 dB | -38±1 dBV | 30 Hz | 2.75 x 1.85 x 0.90mm | Bottom
3SM122KZB1VD-002-R | Analog | 64 dB | 128 dB | -38±1 dBV | <20 Hz | 2.75 x 1.85 x 0.90mm | Bottom
3SM222FMT1WA | Digital | 60 dB | 120 dB | -26±1 dBFS | 38 Hz | 3.10 x 2.50 x 0.90mm | Top
3SM222HMB1WA | Digital | 62 dB | 120 dB | -26±1 dBFS | <20 Hz | 3.10 x 2.50 x 0.85mm | Bottom
3SM222HMB1HA-002 | Digital | 62 dB | 120 dB | -26±1 dBFS | <20 Hz | 3.50 x 2.65 x 0.98mm | Bottom
Notes: 分類
補足料件

## Slide 33: MEMS Microphone Lineup – Consumer
Selection Table |  |  |  |  |  |  | 
P/N | A/D | SNR | AOP | Sensitivity | LFRO | Package | Port
3SM126KZT1VA-002-R | Analog | 64 dB | <20 Hz | -38±1 dBV | 128 Hz | 2.75 x 1.85 x 1.05mm | Top
3SM126KZB1VD-002-R | Analog | 64 dB | <20 Hz | -38±1 dBV | 128 Hz | 2.75 x 1.85 x 0.90mm | Bottom
3SM121MZT1UA | Analog | 66 dB | 130 dB | -38±1 dBV | <20 Hz | 3.76 x 2.95 x 1.10mm | Top
3SM121MZB1UA | Analog | 66 dB | 130 dB | -38±1 dBV | <20 Hz | 3.76 x 3.00 x 1.10mm | Bottom
3SM121LZB1HA | Analog | 65 dB | 130 dB | -38±1 dBV | <20 Hz | 3.50 x 2.65 x 0.98mm | Bottom
3SM221KMT1KA-P | Digital | 64 dB | 120 dB | -26±1 dBFS | 50 Hz | 4.00 x 3.00 x 1.00mm | Top
3SM221KMT1KA-P | Digital | 64 dB | 120 dB | -26±1 dBFS | 50 Hz | 4.00 x 3.00 x 1.00mm | Top
3SM221KMT1GA-P | Digital | 64 dB | 120 dB | -26±1 dBFS | 100 Hz | 4.00 x 2.00 x 1.10mm | Top
3SM222KMB1HA-P | Digital | 64 dB | 120 dB | -26±1 dBFS | 50 Hz | 3.50 x 2.65 x 0.98mm | Bottom
3SM221KMT1KA-P | Digital | 64 dB | 120 dB | -26±1 dBFS | 50 Hz | 4.00 x 3.00 x 1.00mm | Top
3SM123C4T1VA | Analog | 57 dB | 123 dB | -42±1 dBV | 63 Hz | 2.75 x 1.85 x 0.95mm | Top
3SM123GZB1VD | Analog | 61.5 dB | 123 dB | -38±1 dBV | 20 Hz | 2.75 x 1.85 x 0.90mm | Bottom
Notes: 分類
補足料件

## Slide 34: MEMS Microphone Lineup – Consumer
Selection Table |  |  |  |  |  |  | 
P/N | A/D | SNR | AOP | Sensitivity | LFRO | Package | Port
3SM123C4T1VA-022 | Analog | 57dB | 123 dB | -42±1 dBV | 63 Hz | 2.75 x 1.85 x 0.90mm | Top
3SM123GZB1VE-021 | Analog | 61.5 dB | 130 dB | -38±1 dBV | 20 Hz | 2.75 x 1.85 x 0.90mm | Bottom
3SM221KMT1KA | Digital | 64 dB | 120 dB | -26±1 dBFS | 50 Hz | 4.00 x 3.00 x 1.00mm | Top
3SM222KMB1HA | Digital | 64 dB | 120 dB | -26±1 dBFS | 50 Hz | 3.50 x 2.65 x 0.98mm | Bottom
3SM221KMT1KC-P | Digital | 64 dB | 120 dB | -26±1 dBFS | 24 Hz | 4.00 x 3.00 x 1.00mm | Top
3SM221KMT1GC-P | Digital | 64 dB | 120 dB | -26±1 dBFS | 50 Hz | 4.00 x 2.00 x 1.10mm | Top
3SM123GZB1VD | Analog | 61.5 dB | 123 dB | -38±1 dBV | 20 Hz | 2.75 x 1.85 x 0.90mm | Bottom
3SM222KMB1HC-P | Digital | 64 dB | 120 dB | -26±1 dBFS | 30 Hz | 3.50 x 2.65 x 0.98mm | Bottom
3SM222KMB1HC-P | Digital | 64 dB | 120 dB | -26±1 dBFS | 30 Hz | 3.50 x 2.65 x 0.98mm | Bottom
3SM221KMT1KC-P | Digital | 64 dB | 120 dB | -26±1 dBFS | 24 Hz | 4.00 x 3.00 x 1.00mm | Top
3SM221KMT1GC-P | Digital | 64 dB | 120 dB | -26±1 dBFS | 50 Hz | 4.00 x 2.00 x 1.10mm | Top
3SM121KZB1HC | Analog | 64 dB | 120 dB | -38±1 dBV | 30 Hz | 3.50 x 2.65 x 0.98mm | Bottom
Notes: 分類
補足料件

## Slide 35
Sensor
Notes: Kyle DMS ToF Module/LYG / 顆洋/ guesture /
Final PM2.5 / inturrept

## Slide 36
Part Number | Rang distance | VCSEL peak wavelength | Power supply voltage | Operating temperature | Product type
GP2AP02VT20F | 10 ~ 120 cm | 940 nm | 3.3 V | - 20 ~ 70 ℃ | Sensor
GP2AP03VT00F | 0 ~ 10 cm | 940 nm | 3.3 V | - 20 ~ 70 ℃ | Sensor
FSB-004-001AN02 | 0 ~ 10 cm | 940 nm | 3.3 V | - 20 ~ 70 ℃ | Module
FSB-020-001AN06 | 5 ~ 200 cm | 940 nm | 3.3 V | - 20 ~ 70 ℃ | Module
FSB-050-001AN03 | 5 ~ 500 cm | 940 nm | 3.3 V | - 20 ~ 70 ℃ | Module
Cleaning robot
Smart toilet
Attendance machine
Automatic Tap
Capacity detection
Applications
Features
Distance Sensor – ToF
Improved ambient light removal
Notes: 圖換掉

## Slide 37: Distance Sensor - DMS
Item | Parameter
Type | Standard / Compact / Hi-accuracy CMOS
Output type | Analog / I2C / Both / 1bit Hi or Low digital
Cleaning robot
Smart toilet
Attendance machine
Automatic Tap
AGV
Triangulation method
Projector
Robot
Applications
Features
Notes: 加上勝新

## Slide 38: Distance Sensor - DMS Standard
Selection Table |  |  | 
P/N | Measuring range | Size | Output type
GP2Y0A51SK0F | 2 ~ 15 cm | 27×10.8×12t mm | Analog
GP2Y0A41SK0F | 4 ~ 30 cm | 29.5×18.9×13.5t mm | Analog
GP2Y0A21YK0F | 10 ~ 80 cm | 29.5×18.9×13.5t mm | Analog
GP2Y0A02YK0F | 20 ~ 150 cm | 29.5×18.9×21.6t mm | Analog
GP2Y0D21YK0F | 24 cm | 29.5×18.9×13.5t mm | 1bit Hi/Low digital
GP2Y0D02YK0F | 80 cm | 29.5×18.9×21.6t mm | 1bit Hi/Low digital

## Slide 39: Distance Sensor - DMS Compact Connector
Selection Table |  |  |  |  | 
P/N | Measuring range | Size | Average Consumption Current | Distance Measuring Cycle | Output type
GP2Y0AF15* | 1.5 ~ 15 cm | 21.2×8.5×6.3t mm | Typ. 17 mA | Typ. 16.5 ms | Analog
GP2Y0AF30* | 4 ~ 30 cm | 20×8.5×9.0t mm | Typ. 17 mA | Typ. 16.5 ms | Analog
Selection Table |  |  |  |  |  | 
P/N | Measuring range | Size | Current consumption | Measuring time | Accuracy at 50 cm, 25 °C | Output type
GP2Y0E02A | 4 ~ 50 cm | 18.9×8×5.2t mm | 26 mA | Max.40 ms | ± 10% | Analog
GP2Y0E02B | 4 ~ 50 cm | 18.9×8×5.2t mm | 26 mA | Max.40 ms | ± 10% | I2C
GP2Y0E03 | 4 ~ 50 cm | 16.7×11×5.2t mm | 26 mA | Max.40 ms | ± 10% | Analog / I2C
Hi-accuracy CMOS

## Slide 40: Dust sensor
Applications
Item | Parameter
Size | 46×34×12mm
Output interface | UART / I2C
Detectable | PM1.0 / PM2.5 / PM10 separately
Operating supply voltage | 5 ± 0.25 V
Power consumption | Typ 200mW
Sensitivity | ±10%(@PM1.0)
Operating temp. | -10 to 65 °C
Storage temp. | Correction by microcomputer
Equipped with auto cleaning mode function | Yes
Features
Air conditioner
Air purifier
Ventilation system
Consumer electronic products
Air quality monitor
GP2Y1040AU0F

## Slide 41: Dust sensor
Selection Table |  |  |  |  |  | 
P/N | Sensing system | Minimum dust size | Sensing range(TYP) (PM2.5) | Sensitivity accuracy | Output interface | Sensing of each dust size
GP2Y1040AU0F | Particle count | 0.3μm | ～500ug/m3 | ±10% | UART / I2C | ( 1.0 / 2.5 / 10 )
GP2Y1026AU0F | Average density | 0.5μm | ～1000ug/m3 | ±15% | Serial data（UART） | No
GP2Y1014AU0F | Average density | 0.5μm | ～580ug/m3 | 0.5V±15% | Analog voltage | No

## Slide 42: Photointerrupter - Transmissive Type
Applications
Item | Parameter
High operating temperature | -30 to +95°C
Extending area to use photointerrupter under High/Low temperature condition in copier & LBP. | Yes
High reliability of connection improved by combined case & connector as one part. | Yes
Low supply current max. 16.5mA by OPIC output type | GP1A173LCS5F
Features
DLP Project
Lens
Robot
Printer
Water meter

## Slide 43: Photointerrupter - Transmissive Type [Compact type]
Selection Table |  |  |  | 
Model No. | Features | Size | Detecting and Emitting gap (mm) | Slit width (mm)
GP1S092HCPIF | Wide gap, for soldering reflow, surface mount compatible, with positioning boss | 4.5 × 2.6 × 2.9 [height] mm | 2.0 | 0.3
GP1S093HCZ0F | Wide gap | 4.5 × 2.6 × 2.9 [height] mm | 2.0 | 0.3
GP1S094HCZ0F | Wide gap, with positioning pin | 5.5 × 2.6 × 4.8 [height] mm | 3.0 | 0.3
GP1S097HCZ0F | Wide gap, with mounting hole | 4.5 × 2.6 × 4.5 [height] mm | 2.0 | 0.3
GP1S194HCZ0F | Compact, wide gap, | 3.6 × 2.0 × 2.7 (height) mm | 1.7 | 0.3
GP1S195HCPSF | Compact, wide gap, surface mount compatible | 3.4 × 2.0 × 2.7 (height) mm | 1.5 | 0.3
GP1S196HCZ0F | Compact, low profile | 3.1 × 2.0 × 2.7 [height] mm | 1.1 | 0.3
GP1S196HCPSF | Surface mount, for soldering reflow, compact, low profile | 3.1 × 2.0 × 2.7 [height] mm | 1.1 | 0.3
GP1S296HCPSF | Surface mount, for soldering reflow, compact, low profile | 2.5 × 1.8 × 1.9 [height] mm | 1.0 | 0.2
GP1S396HCP0F | Straight lead type, compact, low profile | 2.26 × 1.4 × 1.6 [height]mm | 1.2 | 0.12
GP1S396HCPSF | Surface mount, for soldering reflow, compact, low profile | 2.26 × 1.4 × 1.6 [height] mm | 1.2 | 0.12

## Slide 44: Photointerrupter - Transmissive Type [With connect]
Selection Table |  |  | 
Model No. | Features | Detecting and Emitting gap (mm) | Slit width (mm)
GP1S173LCS2F | High resolution, both-side mounting type | 3.0 | 0.5
Model No. | Features | Detecting and Emitting gap (mm) | Slit width (mm)
GP1A173LCS5F | Snap-in mounting integrated connector type *1 3.3 V / 5 V operation enforced electrostatic discharge (ESD) increased power line noise tolerance | 5.0 | 0.5
OPIC Type
“OPIC” (Optical IC) is a trademark of SHARP Corporation. An OPIC consists of a light-detecting element and signal-processing circuit integrated onto a single chip.

## Slide 45: Photointerrupter - Transmissive Type [Case type OPIC]
“OPIC” (Optical IC) is a trademark of SHARP Corporation. An OPIC consists of a light-detecting element and signal-processing circuit integrated onto a single chip.
Selection Table |  |  | 
Model No. | Features | Detecting and Emitting gap (mm) | Slit width (mm)
GP1A51HRJ00F | Side mounting, with screw hole | 3.0 | 0.5
GP1A57HRJ00F | PWB mounting type, with positioning pin | 10.0 | 1.8

## Slide 46: Photointerrupter - Reflective Type
Applications
Item | Parameter
Wide operation voltage. | Vcc = 3.0 ~ 5.5V
Low current dissipation | Icc = max. 10mA
High resistant to line noize. | Vp-p ≧ 4.0V
Strong for detecting skewed paper | Θ ≧ 55°
High sensitivity type that is resistant to black paper detection. | GP2A430LCS0F
Features
DLP Project
Lens
Robot
Printer
Water meter
GP2A430LCS0F

## Slide 47: Photointerrupter - Reflective Type [Compact type]
Selection Table |  |  |  | 
Model No. | Features | Size | Detecting and emitting Gap (mm) | Slit width (mm)
GP2S700HCP | Compact, long focal distance, surface mounting leadles | 4 × 3 × 2 [height] mm | 4 | 1.5
GP2S60 | Thin, surface mounting leadless type | 3.2 × 1.7 × 1.1 [height] mm | 1 | 1.0

## Slide 48: Photointerrupter - Reflective Type [Case type OPIC]
Selection Table |  |  | 
Model No. | Features | Optimum detecting Distance (mm) | Internal connection diagram
GP2A200LCS0 | Multiple types of paper detectable, light modulation type, with connector, sensitivity adjusted | 5 to 15 | A
GP2A240LCS0F | Applicable to inverter fluorescent lamp, light modulation type, with connector, sensitivity adjusted | 5 to 15 | A
GP2A250LCS0F | Static electricity resistant, applicable to inverter fluorescent lamp, light modulation type, with connector, sensitivity adjusted | 2.5 to 12.5 | A
GP2A451LCS0 | Compact, screw-clamp type, Applicable to inverter fluorescent lamp, Light modulation type, with connector,3.3 to 5.0V operation | 2.5 to 12.5 | D
GP2A25J0000F | Multiple types of paper detectable, light modulation type, with connector, sensitivity adjusted | 3 to 7 | A
GP2A432LCS0F | Compact, screw-clamp type, multiple types of paper detectable, light modulation type, with connector |  | B
GP2A432LCSAF | Compact, hook type, multiple types of paper detectable, light modulation type, with connector |  | B
GP2A430LCS0F | Compact, screw-clamp type, multiple types of paper detectable, light modulation type, with connector, 3.3 to 5V Operation, Low power consumption |  | C
GP2A430LCSAF | Compact, hook type, multiple types of paper detectable, light modulation type, with connector, 3.3 to 5V Operation, Low power consumption |  | C
GP2A431LCS |  |  | C
GP2A25NJJ00 | Multiple types of paper detectable, light modulation type, sensitivity adjusted, improved light-resistance characteristic for inverter lighting, built-in visible light cut filter |  | A
GP2A25DJ000F | Multiple types of paper detectable, light modulation type, with connector, sensitivity adjusted |  | A
GP2A28AJ000F | Multiple types of paper detectable, light modulation type, with connector, sensitivity adjusted, hook type |  | A
Notes: GP2A230LRS0F > GP2A432LCS0F
GP2A230LRSAF > GP2A432LCSAF

## Slide 49: Sensor Product Application Coverage
Notes: Socle這些產品線幾乎囊括了幾乎全部的消費性市場,一部分的車廠,以及健康相關的應用

## Slide 50
Wireless Modules

## Slide 51: Products
With a fresh approach to the radio frequency communication sector, we bring forth innovative wireless communication modules backed by cutting-edge chip design experience and robust technical support from leading semiconductor manufacturers. Our commitment lies in providing state-of-the-art system solutions, peripheral equipment, and audio-visual equipment, focusing on research and development, production, and sales to deliver excellence in connectivity.
Our product line includes the latest in wireless technology standards: IEEE802.11 a/b/g/n/ac/ax, Bluetooth, 4G, NB-IoT, PLC, UWB, millimeter wave, Sub1G, and Zigbee modules. Through our products, we strive to revolutionize the way devices connect and communicate, offering superior performance and reliability.
Notes: Wifi 一致性 LOGO

## Slide 52: Core competitiveness
Excellent Customer Service:
Our commitment extends beyond delivering quality products; we offer flexible design customization for baseboards and I/O interfaces to meet the unique requirements of your applications. Our dedicated team provides comprehensive technical documentation support and assists with product certification processes, ensuring you have a seamless technical cooperation and support agreement with the original manufacturers, every step of the way in your product development journey.
Notes: Wifi 一致性 LOGO

## Slide 53: Application
Consumer Electronics, Commercial equipment, Home appliances, Lighting, Medical devices, Smart city and other application.
Notes: Wifi 一致性 LOGO

## Slide 54: Wi-Fi 4 (+BT) Wireless Module
Wi-Fi 4 (+BT) Wireless Module (REALTEK IC) |  |  |  | 
Model NO | FS-i5188 series | FS-i5189 series | FS-5223 series | FS-i5192 series
Main chip | RTL8188FTV-VQ1 RTL8188FTV-VC RTL8188FTV-VB RTL8188GTV/RTL8188ETV | RTL8189ES-VB RTL8189FTV-VQ1 RTL8189EM RTL8189FTV-VC | RTL8723DS RTL8723FS RTL8723DU | RTL8192FC RTL8192FS/CS
Wi-Fi Standard | Wi-Fi4 (802.11.b/g/n) 2.4GHz |  |  | 
BT Standard | N/A | N/A | 2.1+EDR/3.0/4.2/5.2 | N/A
Bandwidth | HT20 HT20/HT40 | HT20/HT40 |  | 
Antenna | 1T1R |  |  | 2T2R
Interface Wi-Fi/BT | USB2.0 | SDIO2.0 | SDIO2.0/UART USB2.0/PCM | USB2.0 SDIO3.0
Throughput | 72.2Mbps 150Mbps | 150Mbps |  | 300Mbps
IOT Module
4
Notes: Wifi 一致性 LOGO

## Slide 55: Wi-Fi 5 (+BT) Wireless Module
Wi-Fi 5 (+BT) Wireless Module (REALTEK IC) |  |  | 
Model NO | FS-i5811series | FS-i5821 series | FS-5822 series
main chip | RTL8811CU | RTL8821AU RTL8821CE RTL8821CU-VB-CG RTL8821CS RTL8821CSH | RTL8822BS RTL8822CS-VS-CG
Wi-Fi Standard | Wi-Fi5 (802.11.b/g/n/ac) 2.4GHz / 5GHz |  | 
BT Standard | N/A | 2.1+EDR/3.0/4.2/5.0 | 
Bandwidth | HT20/HT40/HT80 |  | 
Antenna | 1T1R |  | 2T2R
Interface Wi-Fi/BT | USB2.0 | USB/USB2.0 PCIe/USB USB3.0/UART | SDIO3.0/UART PCIe/UART PCI/USB
Throughput | 433Mbps |  | 866Mbps
IOT Module
5

## Slide 56: Wi-Fi 6 (+BT) Wireless Module
Wi-Fi 6 (+BT) Wireless Module (REALTEK IC) |  |  | 
Model NO | FS-i5852 series |  | 
main chip | RTL8852BE-VR / RTL8852BS / RTL8852BE-CG / RTL8852BU / RTL8852BS |  | 
Wi-Fi Standard | Wi-Fi6 (802.11.b/g/n/ac/ax) 2.4GHz / 5GHz |  | 
BT Standard | 2.1+EDR/3.0/4.2/5.2 |  | 
Bandwidth | HT20/HT40/HT80 | HT20/HT40/HT80 | HT20/HT40/HT80
Antenna | 2T2R |  | 
Interface Wi-Fi/BT | SDIO3.0/UART PCIe/UART PCIe/USB USB/USB3 |  | 
Throughput | 1200Mbps |  | 
IOT Module
6

## Slide 57: IOT DK Module
IOT DK Wireless Module |  |  | 
Model NO | FS-i5210 series | FS-i5220 series | FS-i5262 series
main chip | RTL8715AH/RTL8710CX/RTL8711AM | RTL8720CF-VA2-CG/RTL8722DM | RTL8762CMF
Wi-Fi Standard | Wi-Fi4 (802.11.b/g/n) 2.4GHz |  | N/A
BT Standard | N/A | BLE4.2 1Mbps BLE5.0 2Mbps | BLE5.0-MESH
Bandwidth | HT20/HT40/HT80 | HT20/HT40/HT80 | HT20/HT40/HT80
Antenna | 1T1R |  | single
Interface Wi-Fi/BT | SDIO/Uart/GPIO/I2C/PWM | SPI/Uart/GPIO/I2C/PWM/USB/SDIO | UART/GPIO/I2C/PWM
Throughput | 150Mbps |  | 2Mbps
IOT Solution

## Slide 58: NB IOT + Wi-Fi + BLE Module
IOT Module
NB IOT + Wi-Fi + BLE Module |  |  | 
Model NO | FS-i5518 series | FS-i5519 series | FS-i5520 series
main chip | RTL9518AM-II2 | RTL9518AM-IIM | RTL9518AQM-II2
NB-IoT | NB ver.R13/R14/R15 (s/w upgrade) Peak Data rate (@NB2; Multi-tone; 2HARQ) DL 126.8 kbps UL 158.5 kbps 700MHz-2.1GHz( Supporting US B103 defined in 3GPP R17 ) |  | 
Wi-Fi Standard | Wi-Fi4 (802.11.b/g/n) 2.4GHz |  | N/A
BT Standard | BLE5.0-MESH |  | 
Bandwidth | HT20/HT40/HT80 |  | 
Antenna | 1T1R |  | 1T1R
Interface Wi-Fi/BT | SDIO/Uart/GPIO/I2C/PWM | SPI/Uart/GPIO/I2C/PWM/USB/SDIO | UART/GPIO/I2C/PWM

## Slide 59: Special specifications and prices for customized needs
IOT Module
Special specifications and prices for customized needs |  |  |  | 
Model NO | FS-i5008 | FS-i5009-PUC | FS-i5106W-R | FS-i5110-C
main chip | BL602 (bouffalolab,cn) | RTL8720 (Realtek) | ASR1606C (asmicro,cn) | LE5010A1 (LinkedSemi,cn)
NB-IoT | N/A | N/A | LTE CATM1,FDDB1/3/5/8,GSM | N/A
Wi-Fi Standard | 802.11.b/g/n |  | N/A | N/A
BT Standard | BLE5.0 | BLE4.2 | N/A | BLE5.0
Bandwidth | HT20/HT40 | HT20/HT40 | HT20/HT40 | N/A
Antenna | 1T1R | 1T1R | 1T1R | 1T1R
Interface Wi-Fi/BT | SDIO/Uart/GPIO/I2C/PWM | PCI-e | SDIO/Uart/GPIO/I2C/PWM | SPI/Uart/GPIO/I2C/PWM/USB/SDIO
Remark | Low prices | Dedicated PCI-e interface | NB and mobile communications | only BLE5.0,Low prices

## Slide 60: Distributors
Worldwide Handler
Local Agent Distributor (US, EU, CN, TW, ASEAN)
Design-in Focus
(*) : Non-franchised
(*)
(*)
Notes: Digi-Key: Rank WW6, 散料 for prototype building
MOUSER: Rank WW9,散料 for prototype building
Worldwide Handler: 分銷產品，目前我們跟FUTURE合作較為緊密；ARROW及WPG均宣稱WW Rank 1大盤商，走貨能力強，均有合作
當地供應商: 能滿足對小型或少量需求客戶
在代理商方面 我們有專門提供給design-in單位的網路平台商-Digikey跟Mouser 也有專門在國際間鋪完成渠道到Future, Arrow, wpg, AVNET等公司 甚至我們在現地也有提供專門功能的現地代理商, 例如大毅專門在空氣相關, Soitech專門在觸控相關

## Slide 61
Branded Business Partners
Notes: 國際間的家電廠例如Panasonic,美的,格麗以及日本美國的廠商, 影像提供硬體提供商例如大華等都是我們的商業夥伴